## Slide 1
Mathematical Modeling &
Control Strategies for
Hybrid Hydrogen Systems
MAT 4901E | June 2026
Student
Ahmet Yeşil
Student No
090220359
Supervisor
Prof. Dr. Semra Ahmetolan
Plug-in FCHEV · PEMFC Modeling · Optimal EMS

## Slide 2
Presentation Outline
01
Motivation & Problem Definition
0:00
02
System Architecture & Selections
1:30
03
Mathematical Models (Vehicle · PEMFC · Battery)
3:30
04
Cost Function Derivation
6:30
05
EMS Strategies (DP · A-ECMS · MPC · BLFS)
9:00
06
Status & MAT 4902E Roadmap
12:30

## Slide 3
Why Hybrid? The Case for FCHEV
PEMFC Alone — Limitations
✕
Slow dynamic response to acceleration
✕
Cannot absorb regenerative braking energy
✕
Frequent load cycling → membrane degradation
→
FCHEV Hybrid — Solution
✓
Li-ion battery handles transient power demands
✓
Battery absorbs regenerative braking energy
✓
FC operates in efficient steady-state band
Key Question: At every instant t, how much power should the FC supply vs. the battery? → This power-split decision rule is the Energy Management Strategy (EMS).

## Slide 4
System Architecture & Selections
Component
Selection
Topology
T4: PEMFC → DC/DC converter → DC bus ← Battery (direct)
Reference Vehicle
2nd-Gen Toyota Mirai (2020+) | m = 1925 kg, P_fc,max = 128 kW
Drive Cycle
2 × WLTP Class 3b (T = 3600 s · 46.5 km · N = 3600 decision points)
PEMFC Model
Mann–Amphlett 0-D Semi-Empirical (GSSEM)
Battery Pack
A123 ANR26650M1B LiFePO₄ | 96s10p | 7.92 kWh | SoC₀ = 0.90
Battery Model
1-RC + Hysteresis Equivalent Circuit (Nejad et al. 2016)
Cost Scenario
Germany 2026: €11/kg H₂ · €0.35/kWh electricity
EMS Strategies
DP · Adaptive ECMS · MPC · BLFS

## Slide 5
Models — Vehicle Dynamics & Power Balance
Longitudinal Dynamics — Wheel Power
DC Bus Power Balance — defines the EMS decision variable u(t) ≡ P_dc(t)
u(t) ≡ P_dc(t) — single decision variable
Once fixed, battery power follows: P_bat = P_load − P_dc
State: x(t) ≡ SoC(t)
One-dimensional optimal control
N = 3600 decision points

## Slide 6
Models — PEMFC Stack (Mann–Amphlett GSSEM)
Three Voltage Loss Mechanisms
Activation V_act
Tafel-type; dominant at low current density
Ohmic V_ohm
Membrane + contact resistance (Mann correlation)
Concentration V_con
Reactant depletion at high current density
η_fc ≈ 0.70 at ~12 kW → ≈ 0.54 at peak (128 kW)
Non-linear efficiency makes optimal split non-trivial.
Cell Voltage (GSSEM):
N_cell = 330 · A = 300 cm² · T = 343 K (isothermal)
H₂ Mass Flow Rate:
LHV_H₂ = 120 MJ/kg | η_fc stored as 1-D lookup table

## Slide 7
Models — Battery (1-RC + Hysteresis)
Why 1-RC + Hysteresis?
LiFePO₄ OCV curve nearly flat between 20%–80% SoC
Standard RC model cannot distinguish SoC in flat region
Hysteresis state tracks charge/discharge reference curves
Nejad et al. 2016: 1.39% mean error — lowest among 10 models
Pack: 960 cells · 96s10p · 316.8 V · 25 Ah · 7.92 kWh
SoC ∈ [0.20, 0.95] | SoC₀ = 0.90 | SoC_target = 0.25
SoC Dynamics (Coulomb Counting):
η_i = 0.995 (coulombic efficiency)
Two-Level Modeling (Onori et al. 2016):
Plant layer: Full 1-RC + Hysteresis model Controller layer: Simplified Rint model (SoC only)
Battery η ≈ 0.87 vs FC η ≈ 0.61 → Battery wins energetically; but cost decides the optimal split.

## Slide 8
Cost Function — The Optimization Objective
Running Cost per Step:
C_fc,k — Hydrogen Cost
Price M_H₂ = €11/kg (Germany 2026)
Derived from FC efficiency map & LHV_H₂ = 120 MJ/kg
Independent of battery state
C_bat,k — Electricity Cost
Price M_ele = €0.35/kWh (Germany 2026)
Direction-dependent round-trip η_eff
Negative during regenerative charging
Total Cost Functional — Principal Mathematical Result (Eq. 24):
γ = 1000 €: penalises SoC_N ≠ 0.25 at magnitude far exceeding expected trip cost (≈5–15 €).

## Slide 9
Four Energy Management Strategies
DP
Dynamic
Programming
Global Benchmark
Bellman backward recursion over full drive cycle. Offline only — cannot be deployed in real vehicle. Serves as theoretical upper bound for all other strategies.
Real-time:
No
Comp. load:
High (offline)
Optimality:
Global
A-ECMS
Adaptive
ECMS
Production Candidate
PMP-based Hamiltonian minimisation at each step. PI feedback on SoC error adapts equivalence factor s(t) online. Near-DP performance in real time.
Real-time:
Yes
Comp. load:
Low
Optimality:
Near-optimal (PMP)
MPC
Model Predictive
Control
Production Candidate
Receding horizon N_p = 15. Solves QP at every sample, applies only first step. Assumes constant future load over prediction horizon.
Real-time:
Yes
Comp. load:
Medium
Optimality:
Local
BLFS
Boundary Layer
Surface Following
Protection Layer
Hysteresis band ±0.05 around SoC_ref. FC ramp ≤ 5 kW/s. Lightweight layer operating beneath A-ECMS or MPC — not a standalone strategy.
Real-time:
Yes
Comp. load:
Very low
Optimality:
Rule-based

## Slide 10
EMS Formulations — DP & Adaptive ECMS
Dynamic Programming — Bellman Backward Recursion
State grid: ΔSoC = 0.005 · Control grid: ΔP_dc = 1 kW · N = 3600 steps (Sundström & Guzzella 2009; Bertsekas 2005)
Adaptive ECMS — Pontryagin's Minimum Principle
Hamiltonian minimised at each step:
Equivalence factor s(t) updated by PI feedback on SoC tracking error:

## Slide 11
EMS Formulations — MPC & BLFS Protection Layer
Model Predictive Control — Receding Horizon (N_p = 15)
At every step k, solve a finite-horizon QP and apply only the first control action:
Assumes constant future load over horizon · Solves QP at every sample · Applies first element only
Boundary Layer Surface Following (BLFS) — Protection Layer
SoC > SoC_ref + 0.05
→
FC at minimum power → battery depletes toward target
SoC < SoC_ref − 0.05
→
FC at peak-efficiency point → battery recharges
SoC inside band [±0.05]
→
Upper-level (A-ECMS or MPC) command passed through
FC ramp rate limited to |dP_fc/dt| ≤ 5 kW/s — prevents membrane degradation (Eq. 31)

## Slide 12
Qualitative Comparison of EMS Strategies (Table 4)
Property
DP
A-ECMS
MPC
BLFS
Information
needed
Full cycle
(offline)
Instantaneous
+ SoC ref.
Finite horizon
N_p = 15
Instantaneous
SoC only
Optimality
Global
optimum
Near-optimal
(PMP)
Local
(horizon)
None
(rule-based)
Real-time
capable
✕ No
✓ Yes
✓ Yes
✓ Yes
Computational
load
High
(offline)
Low
Medium
Very Low
Role in
project
Benchmark
Production
candidate
Production
candidate
Protection
layer

## Slide 13
Current Status & MAT 4902E Roadmap
MAT 4901E — Completed
Literature survey (EMS · PEMFC · Battery)
System architecture fixed (T4 · Mirai II · WLTP)
Longitudinal vehicle dynamics model
Mann–Amphlett GSSEM (PEMFC model)
1-RC + Hysteresis battery model
Power flow model & conversion chains
Cost functional (Eq. 24) derived
Optimal control problem stated (Eqs. 25–26)
All 4 EMS strategies formulated (Eqs. 27–31)
MAT 4902E — Upcoming
1
Python simulation environment (2-layer)
2
PSO/GA parameter identification (Mirai II stack)
3
FC efficiency map (η_fc lookup table)
4
DP implementation (Bellman recursion)
5
A-ECMS with PI-adapted equivalence factor
6
MPC transcribed as quadratic program
7
BLFS integrated beneath A-ECMS & MPC
8
Comparison: cost (€/100 km) · H₂ · electricity
9
Sensitivity analysis (price scenarios + γ)
The complete mathematical formulation is finalized — MAT 4902E is dedicated to numerical implementation & strategy comparison.

## Slide 14
Key Contributions
Plug-in FCHEV modeled on 2nd-Gen Toyota Mirai with rescaled 7.92 kWh LFP pack
Mann–Amphlett GSSEM + 1-RC Hysteresis battery in two-level plant/controller framework
Monetary cost functional (Eq. 24) combining H₂ cost and grid electricity cost
Four EMS strategies formulated: DP · A-ECMS · MPC · BLFS (Eqs. 27–31)
MAT 4902E
Simulation
& Strategy
Comparison
Python · DP · A-ECMS
MPC · BLFS · €/100 km
June 2026 →
Thank you — Questions?
Ahmet Yeşil | MAT 4901E | June 2026 | Supervisor: Prof. Dr. Semra Ahmetolan